## Slide 1
Luna
Heating and cooling

## Slide 2
What is a Luna?
Luna is a ceiling-mounted device for heating and cooling rooms. Designed for use in facilities requiring increased aesthetic values.
Luna units are characterized by a long range and high power, which, combined with advanced automation, guarantees quick achievement of the set temperature even in the case of high rooms.
Intelligent temperature management algorithms combined with a fluent adjustable EC fan guarantee minimal energy consumption.
The innovative, automatically adjustable 360° air supply nozzle guarantees even air distribution, regardless of the operating mode of the device or the height of the room.

## Slide 3
Luna
application
Commercial facilities:
car showrooms, restaurants, gyms, exhibition halls;
Retail industry:
supermarkets;
logistics facilities: distribution centers, warehouses;
medium-sized industrial building

## Slide 4
Heating
Cooling
Recirculation
Destratification
Air filtration (G4 standard filter)
Collaboration with heat sources (e.g. heat pumps)
Device
functions

## Slide 5
Luna units are designed to collaborate with external heat/cool sources, such as heat pumps.
Collaboration with heat pomps

## Slide 6
The air is drawn from above the device by a radial fan. It is then directed to the water heat exchanger and blown into the room through a movable 360° nozzle, at an appropriate angle depending on the device's operating mode.
Luna is designed to operate with recirculated air. However, by providing ventilation channels above the device, it can also work with ventilated or mixed air, enabling collaboration with Cube devices.
Principle of
operation

## Slide 7
Optimal airflow The 360° air nozzle automatically adjusts the direction of airflow based on the device's operating mode. It ensures even distribution of the air stream regardless of the room's height, providing uniform airflow throughout the space.
Principle of
operation

## Slide 8
Airflow - infrared simulation
Bottom air supply
Side air supply
Mixed air supply

## Slide 9
Airflow
- CFD simulation
Boundary conditions:
Temperature difference: 5K
Airflow rate: 3000 m3/h
Room height: 8 m
Air velocity at the edges: 0.5 m/s
Airflow range: 8 m

## Slide 10
Components used
Filter Coarse 70% (~G4)
EPP casing
ABS casing
EC fan
Radial water heat exchanger
Drain tray and condensate pump.
Automatic 360° nozzle.
Lower cover

## Slide 11
Stepless EC fan Luna is equipped with an advanced control system as a standard feature. The smooth regulation of the EC fan speed, based on the temperature difference, ensures minimal energy consumption..
Radial
EC fan

## Slide 12
Plug
and play
Unit is delivered with fully functional controlling system. There is no need of complicated control cabinets.

## Slide 13
Service
access
Easy service Fast service access to components from bottom.
Notes: Aby zdjąc dolną pokrywę należy odkręcić 4 śruby jedna jest imbusowa (allen screw), pozostałe ręcznie. (1 Imbusowa ze względu na przepisy bezpieczeństwa) The lid hangs on a cord with a carabiner. Po zdjęciu pokrywy mamy dostęp do sterownika(drv). Czyszczenie tacy (drain tray) wymaga tighten the next few wing screws (by hand) then we have access to the drain tray and the drain pump.

## Slide 14
Luna 2 H 2-pipe heating unit
Luna 2 HC 2-pipe heating and cooling unit
Luna 4 HC 4-pipe heating and cooling unit
Color options Black and white
Luna Types

## Slide 15
Basic
parameters
Cooling capacity
14,6 kW (7/12° 26° C 55%)
Weigth
33 kg
Heating capacity
32,5 kW (70/50° 16° C)
Range
up to 8,0 m
Airflow
3500 m3/h
Acoustic pressure level
37 - 54 dB(A)
Power supply
230/50 V/Hz
Automatic 360° air nozzle

## Slide 16
Luna
dimensions

## Slide 17
Luna accesories
3-way valve with a 3-point actuator, 230V
2-way valve with an ON/OFF actuator, 230V
room temperature sensor (NTC10K)
drain tray for valve with actuator
blende for suspended ceiling install
filter Coarse 70%
adapter for the ventilation duct (diameter 450mm)
Soon:
Motion sensor
LED ring
Notes: Automatyka jest gotowa na współprace z czujnikiem obecności / czujnikiem ruchu to tryb smart. Na razie sami nie mamy w ofercie takiego czujnika ale może pracować z czujnikiem zewnętrznym

## Slide 18
Luna
accesories
Drain tray
for condensate drainage to the valve and actuator (optional).

## Slide 19
Luna
accesories
Blende for suspended ceiling install (opptional)
Notes: Do urządzenia montowana na wcisk, przyklejana do sufitu na klej.

## Slide 20
Luna
accesories
Filter Coarse 70% (G4) (in standard)
Installation on the top surface of the device.
The filter should be replaced periodically, depending on the level of contamination.

## Slide 21
Installation
options
under the ceiling
in the suspended ceiling
ceiling air intake required

## Slide 22
Installation
options
 | Dimension
A | min. 1 m
B | min. 15 cm
C | min. 2 m
D | max. 8 m*
*depending on the operating mode of the device
Notes: Kluczowy wymiar jak blisko sufitu jesteśmy w stanie zamontować Lunę – 15 cm

## Slide 23
Oznaczenie | Wymiar
A | 548
B | 296
C | 1140
Installation
options
Notes: Mounting pins M8, w zestawie nie mamy śrub ani szpilek, w kartonie nie ma też żadnego wzoru aby ułatwić wiercenie – często o to pytają

## Slide 24
Power supply connection
Notes: Podłaczenie zasialania: Prowadzimy przewód zasialający po szpilce do urządzenia poprzez przygotowane korytko a następnie przez otwór po stronie opisanej wytłoczeniem jak Power Ze sterowaniem podobnie tylko do otworu podpisanego jako control Następnie podpinamy się zgodnie ze schematem do przygotowanych złączek do których dostęp mamy po zdjęciu dolnej pokrywy urządzenia Podłaczenie hydrauliczne poprzez węże elestyczne do króćów w zależności od modelu urządzenia podłączenie wygląda różnie, króćce są opisane wytłoczeniem w EPP a tabela jak podłączyć w DTR

## Slide 25
Controlling of the unit